UFO LED highbay lights Specification

LED bay light of its own characteristics

LED high bay light is to use white LED as a light source, the shell is made of aluminum alloy, with a high-efficiency lens cover, LED highbay light power is only 20% of the sodium, the traditional highbay light 250W and 400W sodium lamps, now uses only 100W of LED highbay light can achieve the same effect, energy saving effect is very obvious, the other due to the traditional highbay light heat large, so often cause damage due to overheating lamps, LED highbay light adopt finned radiator cooling natural air circulation makes more perfect, were circulated outside, effectively guarantee the LED  highbay light will not overheat and damage.

Advantages of LED highbay light,

LED highbay light uses single high power LED as the light source, using a unique multi-chip integrated single source design, selection of imported high brightness semiconductor chips with high thermal conductivity, low luminous decay, pure light color, no ghosting.

2, shell table surface anodic oxidation processing, compact appearance.

3, green pollution-free, lead, mercury and other pollution elements, no environmental pollution.

4, LED mining light color is good, the color rendering of the kind more real, and a variety of light and color options to meet the needs of different environments, eliminating the traditional lamp color temperature depression caused by low mood or, so that the visual comfort, improve people's working efficiency.

5, using the constant current control, the use of wide voltage to overcome the power generated due to the rectifier, noise pollution and instability caused by lighting, to avoid the work to bring the eye irritation and fatigue.

6, simple installation, easy disassembly, using a wide range.

7, high luminous efficiency, more energy, the equivalent of 100W of LED highbay light can replace traditional 250W and 400W sodium lamps.

8, traditional light fixtures have high shortcomings temperature, lighting temperature can reach 200 to 300 degrees. The LED itself is a cold light, lamp temperature is low, more secure.

Applications LED high bay lights

Suitable for factories, warehouses, workshops, supermarkets, museums, stadiums, construction sites and other lighting places.

Datasheet:

| Model | PL-UFO-08S-100W | PL-UFO-08S-150W | PL-UFO-08S-200W |
| --- | --- | --- | --- |
| Power | 100w | 150W | 200W |
| Luminous Flux | 180lm/w±5% |
| LED Source | Samsung 2835SMD |
| Inpuct Voltage | AC100~277V |
| Frequency Range | 50~60Hz |
| Total Harmonic Distortion | <15% (Typical : 8%) |
| Color Temperature | 4000K, 5000k, 5700K |
| Color Rendering Index | CRI>70/80 |
| IP Rating | IP65 |
| Beam Angle | 60/90/110° |
| Optical Transmittance | >97% | >97% | >97% |
| Housing Color | Black/Gray/White |
| Working Life | >50,000 hours |
| Warranty | 5 years |
| Working Environmment | -30ºC~+50ºC, 10%~90% RH |
| Body & Shade Material | Die-casting Aluminum housing & TG glass& Acylic lens |
| Where Can Use | Warehouse; industrial production workshop; pavilion; stadium; the train station; shopping malls; gas stations and other indoor lighting |

Product details

Dimension (unit:mm)

100W Dimension (unit:mm) :280*168mm

150W Dimension (unit:mm):340*174.5mm           2000W Dimension (unit:mm):260.3*194.2mm

Lighting distribution(100W,90degrees)

Installation

Packaging:

| Ltem Model | Cartonsize (cm) | N.W. (kg) | G.W ( kg) | QTY. (PCS) |
| --- | --- | --- | --- | --- |
| PL-UFO-08S-100W | 34*38*19cm | 2.65KG | 3.35KG | 1PCS |
| PL-UFO-08S-150W | 39*39*20cm | 3.90 KG | 4.80 KG | 1PCS |
| PL-UFO-08S-200W | 46*46*19cm | 5.10KG | 6.0KG | 1PCS |

Precautions

1, prior to installation or use, please read the instructions say;

2, when the lamp is working, do not touch;

3, when the lights do not work with water or a wet cloth to wipe lamp

4. Consult require special installation technician or supplier

5, artificial damage in the warranty period, free repair.

Maintenance:

1、The power must be cut off before maintaining.

2、Cleaning the glass of the product in regular time to ensure the good efficiency.

3、Cleaning the housing and radiator in regular time to ensure the good performance of heat sinking.

4、Can use the screwdriver open the cover and take out of the driver to change a new.And connection 	   of the wires of AC driver please follow below:Brown to connect "L",Blue to connect "N",Yellow to 	   connect "",And the red or white wires of DC connect the positive pole of  driver,and the black 	    wire connect the negative pole of driver.and don't mix the positive pole and negative pole.

5、Please take measures of lightning protection, and ensure the Input voltage which is stable.

6、Pls put the lamp under the dry, ventilated and clean circumstance, and clean and maintain regularly.

7、Don’t disassemble by yourself,  avoid the electric shock as there is high voltage inside the lamp.

8  Don’t upside down when installing or lighting the lamp

- Please ask the qualified professional person for help.

Installation

# Warranty

All products use constant current power supply ,and have 5 years warranty（According to your requirement）

Remark:The warranty on the base of right storing way,right installing way,right using way,right maintaining way.Any broken out of our rule,out of our warranty.During the warranty time,we can choose repairing,replacing parts or replacing the whole products according the detail information.And we'll charge the customers some material fee and labor cost if the product out of our warranty time.

Please read the instruction carefully before you use the product.We keep the right of final explanation for the instruction and the product.The product will keep updating continues.And sorry for the no notice for the updating.sure the Input voltage which is stable